## Slide 1
Metastability measurement system
GF180MCU · ECE 298A · Tiny Tapeout
Late clocks · +50 ns / +100 ns
Asynchronous data
Ring oscillator
31 stages
÷4
Source select
External data
Ring or external input
Four test flip-flops
Shared data and capture clock
1
Library reference
dffq_1
2
Baseline
standard-cell flip-flop
3
Our design
one targeted change
4
Control
comparison variant
D
4:1
DUT select
Q[3:0]
2-bit DUT code
Late samples
+50 ns and +100 ns
Settled reference samples
Early sample
At selected delay dₖ
Rising / falling-edge observers
Compare
Early vs. late
Evaluate at +150 ns
Counters
K disagreements
N trials
event
Held 8-bit output
uo[7:0]
BUSY · DONE · FAULT
Sequencer
20 MHz system clock
One trial every 200 ns
Capture clock
clk / rst_n / ena / START / mode
Programmable delay
16 selectable settings
Two interleaved chains
Calibration
Measures each
code’s actual delay
Timing launch
Early clock
4-bit delay code · One shared delay calibration
Data / result
Clock / timing
Off-chip analysis
Sweep the delay
Repeat the measurement for each DUT
Calculate p̂ₖ = K / N
Disagreement rate; N = 255 per block
Fit ln(p̂ₖ) against calibrated delay dₖ
Find the slope of the fitted line
Extract τ = −1 / slope
Compare τ across the four DUTs

## Slide 2
Draft I/O assignment
Tiny Tapeout logical ports
Signal | Dir. | Port assignment
Clock, active-low reset | In | clk, rst_n
Design select [1:0] | In | ui[3] (bit 0), uio[6] (bit 1)
Delay code [3:0] | In | ui[2:0] (bits 2:0), uio[7] (bit 3)
Start, source, data, mode | In | ui[4], ui[5], ui[6], ui[7]
Oscillator enable | In | uio[0]
Held 8-bit result | Out | uo[7:0]
Busy, done, fault | Out | uio[1], uio[2], uio[3]
Source monitor, trial monitor | Out | uio[4], uio[5]
ena is the Tiny Tapeout tile enable. Assignments remain provisional.

## Slide 3
Project schedule
Proposed work periods. Review and submission dates follow the design plan.
Workstream
October 2026
November
Dec
1 Oct
8
15
22
29
5 Nov
12
19
26
3 Dec
7
Milestones
Design review
Timing review
Verification
Target submission
Architecture & experiment plan
Supply check, circuit review, error budget
DUT & sampling-path integration
Delay line, observers, divider, pin mapping
Control & readout RTL
Sequencer, counters, held-count output
Delay & timing validation
Sampling delays, calibration, SPICE checks
Full-system verification
RTL integration and cocotb tests
Layout & final timing checks
Preserve DUT cells and check routed timing
Submission preparation
Final checks, design files, documentation
Proposed work period
Review / submission milestone
Checkpoints
What each review must show
8 Oct
Design review
Architecture, experiment plan and error budget agreed
5 Nov
Timing review
Sampling delays and calibration validated in SPICE
26 Nov
Verification
Full system passes integrated RTL tests
7 Dec
Target submission
Final checks done; design files and documentation submitted